## Slide 1
BOUCHARD
AI-Powered Autonomous Navigation
That Thinks Before It Moves
Dual-layer intelligence: reflexes react, Claude plans.
Named after Hipolito Bouchard, the Argentine corsair who navigated
hostile terrain with strategy and audacity.
Hackathon 2026 | Franco Perez | Webots + Claude AI

## Slide 2
THE PROBLEM
Autonomous robots are bad at
exploring complex environments.
Low coverage
Heuristic navigation (random walk, wall following) leaves large unmapped gaps in multi-terrain arenas
Terrain-blind
Traditional planners treat all surfaces the same — they don't know sand causes slip or ramps need more power
Getting stuck
Robots loop endlessly, revisit already-mapped areas, and miss high-value zones
Incomplete exploration = failed missions (missed victims, blind spots, wasted time)

## Slide 3
THE SOLUTION
Two layers of intelligence working together.
STRATEGY LAYER
Claude AI (periodic, every ~10s)
Analyzes occupancy map
Identifies unexplored frontiers
Plans multi-step sequences
Decides WHERE to explore
REFLEX LAYER
Real-time (every 32ms)
Obstacle avoidance
Terrain classification
Slip compensation
Emergency braking
When strategy and reflexes conflict, REFLEXES ALWAYS WIN. Safe by design.

## Slide 4
HOW IT WORKS
Every 32 milliseconds, a full cycle.
1
SENSE
8 IR + accelerometer
+ gyroscope + encoders
>
2
MAP
60x60 cell grid
(5cm resolution)
>
3
REACT
Reflexes: terrain,
obstacles, slip
>
4
PLAN
Claude analyzes map,
picks frontier
>
5
EXECUTE
Differential drive
follows the plan
Claude Tools (structured, not free-text):
set_exploration_target(x, y) backtrack() patrol_area(x1, y1, x2, y2) investigate(x, y)

## Slide 5
THE ARENA
3x3m multi-terrain arena in Webots.
Terrain
Speed
Challenge
Metal
60%
High traction, smooth surface
Sand
35%
High slip — active compensation needed
Carpet
50%
Stable baseline navigation
Rough
25%
High vibration — stability monitoring
Ramp
30%
Gravity — power adjustment required
Obstacles: oil barrels, traffic cones, wooden boxes, plastic crates

## Slide 6
THESIS
Can an LLM outperform heuristic navigation?
5/5
Terrain types
explored
1.5x
Expected coverage
vs. heuristic fallback
< 2
Stuck/loop events
per 5-min run
<$0.50
Cost per session
(Claude Haiku + cache)
WHY WE EXPECT THIS
Claude targets high-value frontiers, not just the nearest ones
It factors terrain cost into exploration decisions
It chains multi-step exploration plans (A -> B -> C)
Response caching prevents redundant API calls

## Slide 7
TECHNOLOGY
Minimalist, modular stack.
Simulation
Webots R2025a
(free, industry standard)
Robot
e-puck (diff. drive,
8 IR, IMU)
AI
Claude Haiku 4.5
(tool use + caching)
Controller
Python 3.10+
(stdlib only, 0 deps)
Dashboard
React 19 + TypeScript
+ Tailwind + Vite
Communication
HTTP API (8765)
+ WebSocket (8766)
Minimal deps | Modular | Observable (CSV + dashboard) | Fail-safe (works without API key)

## Slide 8
WHAT MAKES IT NOVEL
LLM-powered robotic navigation.
LLM + Robotics
Claude reasons over spatial maps, not just text. First LLM-powered robotic navigation system.
Dual safety
AI plans, reflexes protect. No other system separates these layers this cleanly.
Terrain adaptation
5 terrain types with distinct physics: sand slip, ramp gravity, rough vibration.
Explainable
Claude explains every exploration decision. Real-time dashboard shows everything.
Graceful degradation
Works without API key in fallback mode. The robot never stops operating.
Bouchard is the only system that is both smart AND cheap.

## Slide 9
LIVE DEMO
1
Live autonomous exploration — watch the robot navigate the arena
2
Real-time dashboard — sensors, occupancy map, Claude's decisions
3
Side-by-side comparison — Claude mode vs. heuristic fallback
Same robot. Same arena. Same time.
Let's see what happens when a robot can think.